## Slide 1: MEPDG – Pavement Design
Julie M. Vandenbossche, P.E., Ph.D.
University of Pittsburgh
Transportation Forum
-Infrastructure Renewal in Transportation-
March 23,2013

## Slide 2: Current status of roadways

## Slide 3: Current status of PA roadways

## Slide 4: Current status of PA roadways
57% of Pennsylvania’s roads are in poor or mediocre condition.

## Slide 5: Current status of PA roadways
Driving on roads in need of repair costs Pennsylvania motorists $2.947 billion a year in extra vehicle repairs.

## Slide 6: Current status of roadways

## Slide 7: Current status of roadways
Federal, state, and local = $91 billion annually
“…level of investment is insufficient and still projected to result in a decline in conditions and performance ….”
FHWA estimates $170 billion needed annually to significantly improve conditions and performance.

## Slide 8: Current design method-DARWIN
INPUTS
Slab thickness
k-value
ESAL
Reliability
PCC strength & stiffness
OUTPUT
D PSI
STATISTICAL
REGRESSION
MODEL
www.pavementinteractive.org

## Slide 9
INPUTS
Slab thickness
k-value
ESAL
Reliability
PCC strength & stiffness
OUTPUT
D PSI
STATISTICAL
REGRESSION
MODEL
www.pavementinteractive.org
Current design method-DARWIN

## Slide 10
INPUTS
Slab thickness
k-value
ESAL
Reliability
PCC strength & stiffness
OUTPUT
D PSI
STATISTICAL
REGRESSION
MODEL
www.pavementinteractive.org
Current design method-DARWIN
Based on materials and traffic conditions from
1958-1960

## Slide 11: AASHO Test Traffic
Max Single Axle
Max Tandem Axle
Notes: This is a pictures of the maximum single and tandem axles. The drivers were army recruits who spent the entire time driving in circles. Note, there was not any air-conditioning, nor radios
Trucks were supposed to keep an average speed of 35 mph . There were also supposed to be painted white line in the road that they were supposed to stay on.

## Slide 12: Current traffic stream
Refrigerated Volvohttp://autos.kosmix.com/topic/Semi-trailer_truck

## Slide 13: AASHO Test Traffic
Started Nov. 1958
Loops 3-6:
  6 veh/lane
  10 veh/lane (Jan ‘60)
Operation
  18 hr. 40 min.
  6 days/wk
Total Loads
  1,114,000 Applications
  Avg. ESAL - 6.2 million
  Max ESAL - 10 million (Flex)
Notes: This shows the typical test traffic on the pavement test sections. All test vehicles were trucks. The single axles loads ranged from 900 kg to 13,600 kg (2,000 - 30,000 lbs.); tandem axles loads ranged from 10,890 kg to 21,780 kg (24,000 to 48,000 lbs.). It is important to note that front axles were not considered load axles except in loop 2, lane 1.
Traffic ran on the test loops from November 1958 to December 1960 (25 months). The test vehicles operated for 18 hr. 40 min. per day for 6 days a week. The average speed on the test loops was maintained at approximately 56 km/hr (35 mph). In total, there were 1,114,000 load applications during the 25 months of testing with over 27 million km (17 million miles) driven.

## Slide 14: AASHO Loading Limitations







Data Limits
(AASHO Road Test)
Current
Designs
>100 Million
<2 Million
Axle Load Repetitions
Pavement Thickness
Projection A
Projection C
Projection B
Current design traffic is far beyond road
test limits
Notes: Key Message: We are extending the findings of the AASHO road test data well beyond anything they imagined.
Background Information: This slide demonstrates one of the most serious drawbacks to using the AASHO road test as a basis for the pavement design. The AASHO road test data was based upon less than 2 million axle applications. This information can be projected several different ways as illustrated by Projection A straight line (the increase in traffic gets a proportional increases in thickness). Or by Projection B, that say as the traffic increase the required thickness required increases at a substantial greater rate. Or Projection C, that says the thickness requirement vary with different levels of traffic. Now we design some roads approaching 100 million applications. The bottom line is that we are way beyond the traffic limits in the AASHO road test.
Instructor Notes: Which of these projections is right based upon the road test? [Make sure you wait until someone tries to answer.]

## Slide 15: AASHO road test performance

## Slide 16: AASHO road test performance
85% of the PCC pavement sections were not loaded to failure.

## Slide 17: Materials and design features
Superpave
Finer cements
Lower w/c
Stabilized bases
Select granular fill
1.5 in dowels
Edge drains
Etc….

## Slide 18: New design method - MEPDG
www.darwinme.org

## Slide 19: New design method - MEPDG
Over 100 INPUTS
Pavement structure
Characterize
Axle Loads and Volumes
Temporal material properties
Climate
STRUCTURAL
MODEL
FATIGUE DAMAGE MODEL
TRANSFER FUNCTION
OUTPUTS
Cracking
Faulting
IRI
Stress & Deflection
Chart: Pavement Age
Accumulate damage
Correlate damage to distress

## Slide 20: MEPDG
Time, years
Traffic
No Units
PCC Strength
Base
Modulus
Subgrade
Modulus
CTE
Time
increment
2
8
6
4
0
Applied Research Associates
www.frankoverstreet.com
www.fronterasdesk.org
barkleydevelopmentcompany.net
Notes: This is a good point to bring back this slide to show how the model through the use of the traffic, climate and material models has considered the changing values of each of the parameters.

## Slide 21: Implementation: Benefits
Improved confidence in design
More cost-effective designs
Special analysis capabilities
  Extrapolation for unusual designs
  Complicated rehab designs
  Identify problems with existing designs
  Forensic analyses
  Special loadings
Notes: Key message: These are some of the potential Benefits of MEPDG Implementation.
Background Information: Improved confidence in the chosen design is a result of using: 1) calibrated models representative of local conditions, 2) material and traffic inputs representative of specific project conditions, and 3) local climate at user defined reliability parameters. With these factors generating designs based on sound engineering principles, agencies can have greater confidence in the chosen design functioning as expected (i.e., lasting for the prescribed life-span).
Cost effective designs will be achieved as a result of fewer over- or under-designs.
Probably the greatest benefit is the flexibility to consider special analyses. Forensic studies, such as evaluation of changes in features from the original design and their impact on distress predictions, can be performed easily. Special loading conditions can be modeled to consider impact on performance. In addition to those listed on this slide, the MEPDG accommodates defensible specification limits and pay factors, since changes in material properties or construction conditions can be evaluated immediately to determine anticipated impact on performance. The user has a great deal of flexibility in using the MEPDG for a variety of studies and evaluations.
Instructor Notes: Build Slide – Ask participants what they believe are possible benefits to implementation. Then go through those already identified and review them with the participants. See if this prompts other ideas and add them to the whiteboard list.

## Slide 22: Agency implementation options
Central office
Districts
Multilevel adoption
  Design catalogues (developed using MEPDG)
    Most roadways:
  MEPDG designs
    High volume roadways
    Non-standard materials/pave. design features
Notes: Key Message: Step 3 covers Development of the Database to define local conditions, which is required for calibration and validation of the models in the MEPDG.
Background Information: As discussed in Lesson 6.1, development of a database that catalogues the range of conditions in an agency will be a key component in the calibration and validation of the models in the MEPDG. The data set may be composed of two distinct types of information. For short term, or “immediate” needs, section information for existing, in-service conditions can be documented, using estimates of material properties or conditions where necessary to fill out the data set. The key to this will be the availability of time series performance data to compare to MEPDG predictions over time. If time-series data collection exists, then efforts should be made to use these sections to validate the model predictions.
In addition, new sections may be monitored, allowing the agency to define all MEPDG input parameters at the onset of the performance monitoring period. This will require a long term commitment to this effort, but is the only true way to calibrate the models to local conditions.
Consideration may be given to use of accelerated pavement testing methods as a means of calibrating the MEPDG as well. Data from an accelerated loading facility or test track may be used to compare actual to predicted performance very quickly. This allows the controlled testing of a pavement section and determination of the material properties for validation in a relatively short period of time. Caution will have to be used to ensure that the results from accelerated testing are representative of true field performance. Accelerated pavement testing provides one alternative for short term results.

## Slide 23: Implementation
Over 100 INPUTS
Pavement structure
Characterize
Axle Loads and Volumes
Temporal material properties
Climate
STRUCTURAL
MODEL
FATIGUE DAMAGE MODEL
TRANSFER FUNCTION
OUTPUTS
Cracking
Faulting
IRI
Stress & Deflection
Chart: Pavement Age
Accumulate damage
Correlate damage to distress

## Slide 24: Implementation
Over 100 INPUTS
Pavement structure
Characterize
Axle Loads and Volumes
Temporal material properties
Climate
STRUCTURAL
MODEL
FATIGUE DAMAGE MODEL
TRANSFER FUNCTION
OUTPUTS
Cracking
Faulting
IRI
Stress & Deflection
Chart: Pavement Age
Accumulate damage
Correlate damage to distress

## Slide 25: Implementation process 1. Database development
Materials
  Surface, base, subbase and subgrade
  Determine default properties
Notes: Key Message: Step 3 covers Development of the Database to define local conditions, which is required for calibration and validation of the models in the MEPDG.
Background Information: As discussed in Lesson 6.1, development of a database that catalogues the range of conditions in an agency will be a key component in the calibration and validation of the models in the MEPDG. The data set may be composed of two distinct types of information. For short term, or “immediate” needs, section information for existing, in-service conditions can be documented, using estimates of material properties or conditions where necessary to fill out the data set. The key to this will be the availability of time series performance data to compare to MEPDG predictions over time. If time-series data collection exists, then efforts should be made to use these sections to validate the model predictions.
In addition, new sections may be monitored, allowing the agency to define all MEPDG input parameters at the onset of the performance monitoring period. This will require a long term commitment to this effort, but is the only true way to calibrate the models to local conditions.
Consideration may be given to use of accelerated pavement testing methods as a means of calibrating the MEPDG as well. Data from an accelerated loading facility or test track may be used to compare actual to predicted performance very quickly. This allows the controlled testing of a pavement section and determination of the material properties for validation in a relatively short period of time. Caution will have to be used to ensure that the results from accelerated testing are representative of true field performance. Accelerated pavement testing provides one alternative for short term results.

## Slide 26: Implementation process 1. Database development
Concrete material properties (WO #13 Sensitivity analysis)
CTE: (WO#13 & LTPP)
  Define for each quarry/pit (Needed)
Strength/Stiffness: (WO#13)
  Strength/stiffness at 1, 3, 7, 28 and 90 days
Drying shrinkage (WO#13 & WO#6)
  Irreversible (Needed)
  Reversible (Needed)

## Slide 27: Implementation process 1. Database development
Built-in Gradient for 5 regions:

## Slide 28: Implementation process 1. Database development
Month of Construction/ Climatic Region | March | April | May | July | Sep. | Oct. | Nov.
Region I | -1.0 | -0.5 | -0.3 | 0.3 | 0.6 | 0.5 | 0.3
Region II | -1.3 | -0.9 | -0.3 | 0.1 | 0.5 | 0.3 | 0.0
Region III | -1.2 | -0.7 | -0.3 | 0.0 | 0.6 | 0.5 | 0.1
Region IV | -1.0 | -0.6 | -0.1 | 0.3 | 0.6 | 0.5 | 0.1
Region V | -1.3 | -1.0 | -0.6 | 0.0 | 0.5 | 0.4 | 0.0
Built-in Gradient for 5 regions:
University of Pittsburgh WO#13

## Slide 29: Implementation 1. Database development (cont.)
Traffic (WO #13)
    10 WIM/AVC:
    AADTT
    Vehicle class distribution
    Hourly distribution factors
    Axle/load distribution factors
Chart: Time, (Hour)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
I-80E | 0.014731 | 0.012405 | 0.0096139 | 0.01256 | 0.009769 | 0.01163 | 0.01349 | 0.02543 | 0.030702 | 0.03675 | 0.043883 | 0.04869 | 0.055823 | 0.058924 | 0.059079 | 0.065281 | 0.065902 | 0.066367 | 0.068228 | 0.066367 | 0.063111 | 0.064041 | 0.05055 | 0.046674
PA-15 | 0.0077008 | 0.015402 | 0.014301 | 0.012101 | 0.0077008 | 0.012101 | 0.011001 | 0.014301 | 0.024202 | 0.019802 | 0.031903 | 0.036304 | 0.041804 | 0.047305 | 0.047305 | 0.057206 | 0.061606 | 0.073707 | 0.060506 | 0.083608 | 0.081408 | 0.079208 | 0.077008 | 0.082508
I-80W | 0.019691 | 0.01367 | 0.014321 | 0.010415 | 0.010578 | 0.011229 | 0.014158 | 0.017738 | 0.02441 | 0.0345 | 0.047681 | 0.048657 | 0.060862 | 0.060862 | 0.063792 | 0.056469 | 0.051912 | 0.070789 | 0.072905 | 0.069325 | 0.067535 | 0.058747 | 0.053377 | 0.046379
I-76 | 0.020238 | 0.023545 | 0.015212 | 0.015344 | 0.0095238 | 0.014286 | 0.016138 | 0.019841 | 0.030159 | 0.041667 | 0.051058 | 0.053307 | 0.050529 | 0.053042 | 0.063228 | 0.056878 | 0.062566 | 0.062566 | 0.063624 | 0.062434 | 0.058466 | 0.05754 | 0.0513 | 0.0475
MEPDG | 0.023 | 0.023 | 0.023 | 0.023 | 0.023 | 0.023 | 0.023 | 0.05 | 0.05 | 0.05 | 0.059 | 0.059 | 0.059 | 0.059 | 0.059 | 0.059 | 0.059 | 0.046 | 0.046 | 0.046 | 0.046 | 0.031 | 0.031 | 0.031
Chart: Principal Arterial and Interstate (TTC 1)
| 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13
TTC 1 | 0.013 | 0.085 | 0.028 | 0.003 | 0.076 | 0.74 | 0.012 | 0.034 | 0.006 | 0.003
PA-15 | 0.014355 | 0.091787 | 0.018496 | 0.010214 | 0.040028 | 0.743 | 0.0097999 | 0.030504 | 0.0033126 | 0.0015183
I-80W | 0.0076392 | 0.068161 | 0.020993 | 0.0080538 | 0.019098 | 0.78216 | 0.0090309 | 0.047642 | 0.016759 | 0.0012436
I-76 | 0.0046541 | 0.081776 | 0.021424 | 0.0033571 | 0.042315 | 0.75788 | 0.004471 | 0.052645 | 0.015382 | 0.0010529
I-80E | 0.0074314 | 0.063342 | 0.019166 | 0.016465 | 0.01706 | 0.79835 | 0.0058596 | 0.051913 | 0.014146 | 0.00088505
Default values represent WIM data
Notes: Key Message: Step 3 covers Development of the Database to define local conditions, which is required for calibration and validation of the models in the MEPDG.
Background Information: As discussed in Lesson 6.1, development of a database that catalogues the range of conditions in an agency will be a key component in the calibration and validation of the models in the MEPDG. The data set may be composed of two distinct types of information. For short term, or “immediate” needs, section information for existing, in-service conditions can be documented, using estimates of material properties or conditions where necessary to fill out the data set. The key to this will be the availability of time series performance data to compare to MEPDG predictions over time. If time-series data collection exists, then efforts should be made to use these sections to validate the model predictions.
In addition, new sections may be monitored, allowing the agency to define all MEPDG input parameters at the onset of the performance monitoring period. This will require a long term commitment to this effort, but is the only true way to calibrate the models to local conditions.
Consideration may be given to use of accelerated pavement testing methods as a means of calibrating the MEPDG as well. Data from an accelerated loading facility or test track may be used to compare actual to predicted performance very quickly. This allows the controlled testing of a pavement section and determination of the material properties for validation in a relatively short period of time. Caution will have to be used to ensure that the results from accelerated testing are representative of true field performance. Accelerated pavement testing provides one alternative for short term results.

## Slide 30
Traffic: (Needed)
  Roadways servicing special industry (such as mining, farming, etc.)
    vehicle class distributions
    axle load spectra based on the industry the roadway services.
Implementation 1. Database development (cont.)

## Slide 31
Climate: (Needed)
  Validate climatic databases
    23 climatic stations in MEPDG
    Compare predicted cracking/faulting
Implementation 1. Database development (cont.)

## Slide 32: Implementation 1. Database development (cont.)
Distress/Performance
  LTPP (Unavailable)
  Local test sections (Needed)
Notes: Key Message: This is a continuation of Step 3, covering development of a database for calibration and validation of the MEPDG Models.
Background Information: As with materials and traffic, proper definition of distress development over time will require a commitment to long term performance monitoring. Existing LTPP test sections may be useful for this purpose. Other studies conducted by agencies in the past may provide valuable information. It is anticipated that there will be limited amounts of information available. The LTPP program was developed because there was a lack of consistent available information of this type.
Studies should seek to record performance of both new and rehabilitated pavement sections. As the pavement infrastructure continues to age, agencies are faced more and more with rehabilitation of an existing facility (more than construction of a new facility). Methods for evaluation of the existing condition and definition of existing material properties need to be developed consistent with the models in the MEPDG.

## Slide 33: Implementation
Over 100 INPUTS
Pavement structure
Characterize
Axle Loads and Volumes
Temporal material properties
Climate
STRUCTURAL
MODEL
FATIGUE DAMAGE MODEL
TRANSFER FUNCTION
OUTPUTS
Cracking
Faulting
IRI
Stress & Deflection
Chart: Pavement Age
Accumulate damage
Correlate damage to distress

## Slide 34: Implementation 2. Calibration / Validation
Local Calibration and Validation
  State materials and performance data
  Eliminate or reduce distress model bias for local conditions
Notes: Key Message: Step 5, Calibration and validation of the MEPDG models, was discussed in detail in Lesson 6.1. It is an important and integral part of the implementation process if a user is to be confident with the results of the analysis.
Background information: As previously recognized, in order for the models to be used with confidence, there must be a collection of agency specific information and a comparison of this information to the predictions of the MEPDG in the form of a validation / calibration exercise. This exercise will allow the MEPDG models to more appropriately represent the agency sensitivities and conditions.

## Slide 35: National field calibration process
Predicted Performance
Actual Field Performance
b
n
Line of Equality
b
n
= National Calibration Factor
Notes: Bn = National Field Calibration Factor

## Slide 36: National calibration states
LTPP
RPPR
LTPP &
RPPR
FL
CA
WA
CA
ID
NV
OK
SD
CO
KS
NE
AR
MN
IN
IA
WI
OH
MI
MS
AL
GA
WV
OH
NY
NJ
www.fhwa.dot.gov
Notes: LTPP 145 sections in 23 states
RPPR 143 sections in 12 states—Expands to 578 observations
  Random joint spacing—separate out by joint spacing
  2 observation for some sections (1987 and 1992)

## Slide 37
Chart: Pavement age, years
Manual Survey Distressed Section | 0.03
Manual Survey Control Section | 0.04
Implementation 2. Calibration / Validation

## Slide 38
Populate database with local test sections:
Cracking/Faulting model calibration:
  Location, date/time of construction, design and layers properties
  Traffic data
  Material characterization
    FWD
    Laboratory testing
  Distress date:
    Manual vs automated
    Faulting and transverse cracking
Implementation 2. Calibration / Validation

## Slide 39: Implementation 3. Revisions to Pub 242
New designs
  Materials, traffic and climate
Overlay designs
  Materials, traffic and climate
Notes: Key Message: Step 6, Parallel Designs. In order to properly verify that the MEPDG is providing reasonable results for an agency, it is recommended that a program of parallel designs be considered for a period of at least two years.
Background information: A parallel design approach will allow a State to become familiar and confident with the predictions and sensitivities of the MEPDG over time, and in consideration of the typical design processes currently existing. Dramatic differences (such as a suitable design by normal standards of practice in the agency, compared to a prediction of early failure by the MEPDG) might be investigated to see why a large disparity exists. This could lead to more specific performance monitoring, recognizing a particular bias in the MEPDG models or material characterizations.
As stated on the slide, it is recommended that this approach be started with a year of parallel designs, using the State approach as the primary and the MEPDG method as a comparative. Any gross differences should be scrutinized to determine the reason for the difference and to make sure that the MEPDG was properly used. This would be followed by another year of parallel designs, using the MEPDG as a primary tool and comparing it to requirements by the standard of practice in the agency. At this point it would be hoped that lessons learned from the first year, and additional knowledge gained for property inputs that accurately reflect local conditions, would be incorporated into the process, thus reducing bias in the results of the MEPDG.

## Slide 40: Implementation 4. Parallel Designs
One year of current procedure designs with MEPDG designs as concurrence
One year of MEPDG designs with current procedure designs as concurrence
Full implementation
Notes: Key Message: Step 6, Parallel Designs. In order to properly verify that the MEPDG is providing reasonable results for an agency, it is recommended that a program of parallel designs be considered for a period of at least two years.
Background information: A parallel design approach will allow a State to become familiar and confident with the predictions and sensitivities of the MEPDG over time, and in consideration of the typical design processes currently existing. Dramatic differences (such as a suitable design by normal standards of practice in the agency, compared to a prediction of early failure by the MEPDG) might be investigated to see why a large disparity exists. This could lead to more specific performance monitoring, recognizing a particular bias in the MEPDG models or material characterizations.
As stated on the slide, it is recommended that this approach be started with a year of parallel designs, using the State approach as the primary and the MEPDG method as a comparative. Any gross differences should be scrutinized to determine the reason for the difference and to make sure that the MEPDG was properly used. This would be followed by another year of parallel designs, using the MEPDG as a primary tool and comparing it to requirements by the standard of practice in the agency. At this point it would be hoped that lessons learned from the first year, and additional knowledge gained for property inputs that accurately reflect local conditions, would be incorporated into the process, thus reducing bias in the results of the MEPDG.

## Slide 41: Additional consideration…..
Notes: Key Message: Step 6, Parallel Designs. In order to properly verify that the MEPDG is providing reasonable results for an agency, it is recommended that a program of parallel designs be considered for a period of at least two years.
Background information: A parallel design approach will allow a State to become familiar and confident with the predictions and sensitivities of the MEPDG over time, and in consideration of the typical design processes currently existing. Dramatic differences (such as a suitable design by normal standards of practice in the agency, compared to a prediction of early failure by the MEPDG) might be investigated to see why a large disparity exists. This could lead to more specific performance monitoring, recognizing a particular bias in the MEPDG models or material characterizations.
As stated on the slide, it is recommended that this approach be started with a year of parallel designs, using the State approach as the primary and the MEPDG method as a comparative. Any gross differences should be scrutinized to determine the reason for the difference and to make sure that the MEPDG was properly used. This would be followed by another year of parallel designs, using the MEPDG as a primary tool and comparing it to requirements by the standard of practice in the agency. At this point it would be hoped that lessons learned from the first year, and additional knowledge gained for property inputs that accurately reflect local conditions, would be incorporated into the process, thus reducing bias in the results of the MEPDG.

## Slide 42: What is CTE
Coefficient of Thermal Expansion – how size of an object changes w/ temp
Property of concrete
Slab expansion/contraction and curling
Impact Pavement Performance
www.tecnocentro.it
lecture.civilengineeringx.com

## Slide 43: Measuring CTE
www.concreteconstruction.net
Testing Procedure: AASHTO T336
Spring Loaded LVDT
4” Dia. Core
Testing Frame
Specimen:
  4 in dia. cores/cylinders
  ~ 6 to 8 in. long
Place in testing frame and submerge in water
Increase water temp to 50°C (120°F) – meas. length
Decrease water temp to 10oC (50oF) – meas. Length
Increase water temp to 50°C (120°F) – meas. length
*Must correct to account for thermal deformation of the frame using calibration specimen
University of California Pavement Research Center

## Slide 44: Error in estimating CTE
CTE of 304 SS calibration specimen was inaccurate over typical PCC service temperatures
  0oC – 500oC → 17.3*10-6/oC
  10oC – 50oC → 15.8-16.2*10-6/oC
Steel CTE too high → PCC CTE to high
LTPP database populated w/ incorrect CTEs
Recalibrate with correct CTEs

## Slide 45: Recalibration
NCHRP Project 20-07/Task 288 initiated
Recalibrated:
  JPCP (transverse cracking and faulting)
  CRCP (crack width and punchout)
Task 288 models:
  PCC thickness designs should be similar to original models
  New calibration coefficients not implemented due to discrepancies in thickness designs

## Slide 46: Resolution
NCHRP Project 20-07/Task 327
Objective:
Conduct an evaluation of recalibration effort under Task 288
Recommend recalibrated models that use accurate CTE values for incorporation into ME design software